## Slide 1
Finite Element Method:
A Homemade
2D Solver
Vasiliy Tereshkov
https://github.com/vtereshkov/fem

## Slide 2: Topics
Editor
Mesh generation
FEM solver
Visualization
Self-check
Implementation

## Slide 3: Editor: Requirements
2D plate boundary: one non-self-intersecting polygon
Holes: only polygons, no circles
Extra points for manual mesh refinement
Constraints: each fixing a point in both X and Y
External loads: only forces, no torques
Material: Young modulus, Poisson ratio, max stress

## Slide 4: Editor: GUI

## Slide 5: Editor: Clockwise or counter-clockwise?
Boundary: counter-clockwise
Holes: clockwise

## Slide 6: Mesh generation: Delaunay triangulation
Good
Bad
Source: https://en.wikipedia.org/wiki/Delaunay_triangulation
Point
inside
How to avoid extremely long and thin triangles?

## Slide 7: Mesh generation: Bowyer-Watson algorithm
Start with a fake super-triangle

## Slide 8: Mesh generation: Bowyer-Watson algorithm
Point 1
Add points one by one

## Slide 9: Mesh generation: Bowyer-Watson algorithm
Point 2
Add points one by one

## Slide 10: Mesh generation: Bowyer-Watson algorithm
Point 3
Two triangles
are no longer
Delaunay

## Slide 11: Mesh generation: Bowyer-Watson algorithm
Remove bad triangulation
Point 3

## Slide 12: Mesh generation: Bowyer-Watson algorithm
Point 3
Retriangulate bad polygon

## Slide 13: Mesh generation: Bowyer-Watson algorithm
Point 4
Add points one by one

## Slide 14: Mesh generation: Bowyer-Watson algorithm
Remove the super-triangle

## Slide 15: Mesh generation: Missing edges
Source: https://gwlucastrig.github.io/TinfourDocs/DelaunayIntroCDT/index.html

## Slide 16: Mesh generation: Missing edges
Source: https://gwlucastrig.github.io/TinfourDocs/DelaunayIntroCDT/index.html
Zooming in

## Slide 17: Mesh generation: Missing edges: Sloan algorithm
Retriangulate bad quad by swapping its diagonals

## Slide 18: Mesh generation: Missing edges
No longer Delaunay, but who cares if we need this edge?

## Slide 19: Mesh generation: Removing outside triangles
Convex hull triangulation: boundaries ignored

## Slide 20: Mesh generation: Removing outside triangles
Outside
Outside
Inside
Outside
Outside

## Slide 21: Mesh generation: Removing outside triangles

## Slide 22: Mesh generation: Removing outside triangles
Zooming in

## Slide 23: Mesh generation: Removing outside triangles
First outside triangle: contains a boundary segment, but in opposite direction

## Slide 24: Mesh generation: Removing outside triangles
Next outside triangle(s): all neighbors, except the inside triangles

## Slide 25: Mesh generation: Removing outside triangles
Remove recursively!

## Slide 26: Mesh generation: Validation
Boundary:
  No intersections
  Each point must belong to 0 or 2 edges
Mesh:
  Each point must belong to a triangle

## Slide 27: FEM: Discretization
∞ points
N points (nodes)
∞ unknown displacements
2N unknown displacements
Interpolate in between

## Slide 28: FEM: Constraints
No displacement
No DOF
No equation
No reaction force

## Slide 29: FEM: Triangular element
unknown independent displacements (DOFs)
q =
external forces (0 if not set)
F =

## Slide 30: FEM: Triangular element: “Hooke’s law”
q
F
?
q
F
Source: https://en.wikipedia.org/wiki/Stiffness
kq = F
1 DOF:
6 DOFs:

## Slide 31: FEM: Triangular element: “Hooke’s law”
In scalar form:

## Slide 32: FEM: Triangular element: Stiffness matrix
6×6 matrix
Indexed by element DOFs
Depends on triangle sides, material and thickness
Explicit formula in fem::createElement()
= force
needed to make

## Slide 33: FEM: Triangular element: Stiffness matrix

## Slide 34: FEM: Connecting elements
Element: 6 DOFs
Whole model: 2N DOFs
Element DOF
(0…5)
Global DOF
(0…2N—1)

## Slide 35: FEM: Global stiffness matrix
2N×2N matrix
Indexed by global DOFs
Made of element stiffness matrices

## Slide 36: FEM: Global stiffness matrix
K = 0
for each element
for each i
for each j
Element DOF
i
j
Global DOF
m
n
Pseudocode:

## Slide 37: FEM: Global stiffness matrix

## Slide 38: FEM: Constraints
Constrained DOF
Constrained DOFs? Just strike them out!

## Slide 39: FEM: Constraints
After r constrained DOFs removed:
(2N — r) × (2N — r) matrix
Non-degenerate: can solve for q

## Slide 40: FEM: Displacements
Solve for q
1 DOF:
q = F / k
(2N — r) DOFs:

## Slide 41: FEM: Displacements: Gaussian elimination
Don’t want to inverse K’? Solve K’q = F directly
Example: 2 unconstrained DOFs
How many (1)s do we subtract from (2) to eliminate
(1)
(2)
?
Answer:

## Slide 42: FEM: Displacements: Gaussian elimination
Find
, then
0

## Slide 43: FEM: Stresses
Displacements interpolated linearly
Constant strain over element
Constant stress over element
Constant color in stress visualization

## Slide 44: FEM: Stresses
Explicit formula in fem::getEquivalentStress()
3 stresses responsible for 3 “elastic” DOFs
X tension
Y tension
Shear

## Slide 45: FEM: Stresses
Explicit formula in fem::getEquivalentStress()
Von Mises equivalent stress
X tension
Y tension
Shear

## Slide 46: Visualization

## Slide 47: Self-check
Not stressed?!
Compression
Tension
Not stressed!
Beam bending

## Slide 48: Implementation
Umka: a statically typed embeddable scripting language
tophat: a 2D framework for making games in Umka
https://github.com/vtereshkov/umka-lang
https://tophat2d.dev/

## Slide 49: Questions?